## Slide 1: Smartbuilding
Marcin Bajer Kraków, 03.09.2015

## Slide 2: Project idea
Project goal is to prepare home automation for medium size rent building/hotel (12 flats).
Off-the-shelf hardware is used (i.e. Arduino/Raspberry Pi/TP-Link TL-WDR4300 routers).
The center of the project is RaspberryPi running the custom prepared web server (node.js based) and some of generic applications (PostgresSQL, Radius server, syslog server, DHCP, DNS…).
In the building there is also a few TP-Link TL-WDR4300 routers (OpenWRT running) which are used not only to provide WiFi, but also as hubs for smart home automation devices.
Virtual USB tunnel is established between TP-Link router and RaspberryPi so USB devices connected to router are seen by the node.js server as if there were directly connected to RaspberryPi.

## Slide 3: Stage 1 – Network access control and monitoring
…
…

IP camera

Internet
Guest 1


Guest 2
…
Guest 3
Administrator
Guest network WiFi
(WPA-2 Enterprise)
Admin network WiFi
(WPA-2 PSK)
DHCP
DNS
Radius server
Node.js server
Syslog.ng server
OpenVPN
Access Point
Access Point
Access Point
Router

## Slide 4: Step 2 – Smart building automation
…
Virtual USB
JSON API
USB
1wire
I2C
USB


Actuators
Sensors
Motion
Detectors
Intercom
RS232
Electricity
meter
RS232
(IEC 61107)
Access
control
RS485
Temperature

Light sensor
…
Control
board


Visualization
(web page)

IP camera
ONVIF
WiFi
(WPA-2 Enterprise)

Internet
Visualization
(external web page)
OpenVPN